## Slide 1
Open
Load
Run
Frame per second:
XXX
(to be given by the user)
Fluorescent signal intensity vs Time (∆I / ∆t)
Fluorescent signal intensity vs Time
Save as
Export Data
Save as
Export Data
Permeability coefficinet
ROI 1
∆I / ∆t =
∆I / ∆t =
∆I / ∆t =
=
Vessel Diameter (D) = cm
P = D/4 * *∆I / ∆t = cm/s
ROI 2
∆I / ∆t =
=
Vessel Diameter (D) = cm
P = D/4 * *∆I / ∆t = cm/s
ROI3
∆I / ∆t =
=
Vessel Diameter (D) = cm
P = D/4 * *∆I / ∆t = cm/s
ROI 4
∆I / ∆t =
=
Vessel Diameter (D) = cm
P = D/4 * *∆I / ∆t = cm/s
Save as
Export Data
Average P = cm/s

## Slide 2
Permeability coefficient through vessel wall (cylindrical structure)
Permeability Coefficient
Vessel Surface
Vessel volume
Maximum fluorescent dye intensity at time 0
(inside the vessel/for normalization/constant)
Fluorescent signal intensity vs Time
Fluorescent signal intensity vs Time (1/s)
cm/s
As the network of the vessels is non-homogenous, quantifying this coefficient must be regional following the process on the next slide

## Slide 3
Soheila’s manual method to calculate the permeability coefficient
ROI1
ROI2
ROI4
ROI3
ROI1
D/2 (cm) 0.0019
Slope (∆I/∆t) 4.20 (using Fiji and based on the mean fluorescent intensity of the region inside the ROI1 polygonal vs time)
I0 746
P (cm/s) 1.07e-5
The same process to be applied for the other regions of interest (min. 4 regions) and the average to be considered as the permeability coefficient.